## Slide 1
Causal Discovery on Tennessee Eastman:
PCMCI+, VAR-LiNGAM and LSTE
What the data told us before we ran anything, and whether the results agreed
Tennessee Eastman · 31 variables × 1499 samples · commit e8f02e8
The exploratory analysis predicted a distinct failure mode for each method. Three of the four predictions held; the fourth failed in the opposite direction, and that is the finding.
EDA eda-20260831-005002
run run-20260831-025032
LSTE run-20260831-025653
Notes: Tennessee Eastman, 31 variables, 1499 samples. Everything in this deck comes from two runs in the repo; the run IDs are on the slide.

## Slide 2
OBJECTIVE
2
What we set out to do, and the 16 runs we did it with
Recover the causal graph over Tennessee Eastman process variables from observation alone, and score the recovery against the benchmark's published ground truth.
HOW THE WORK WAS SEQUENCED
Characterise
31 x 1499 measured
against every assumption
Choose
tau, alpha and scaling
read off the EDA
Run
4 methods
16 configurations
Score
SHD against the
30-edge projected truth
THE SCOPE OF THIS DECK, IN FOUR NUMBERS
3
methods announced
PCMCI+, VAR-LiNGAM, LSTE
+1
baseline
PC, the i.i.d. reference point
16
scored configurations
3 PC, 6 PCMCI+, 6 VAR-LiNGAM, 1 LSTE
30
edges in the target
latent projection of a 32-edge truth
SHD counts a missing, extra or reversed edge as 1 and an unoriented edge as 0.5: a CPDAG's undirected edge is an abstention, not an error. Two ground-truth nodes (X27, X31) have no column in the data, so the truth is projected onto the 31 observed variables before anything is scored.
[8] Menghi et al., arXiv:2208.01529, 2022 - CIPCaD-Bench
Notes: Three methods were announced last time: PCMCI+, VAR-LiNGAM, LSTE. PC is here as the i.i.d. baseline - it is what the temporal methods are supposed to improve on, so it has to be in the table.

## Slide 3
STATE OF THE ART
3
Four methods that disagree about what the data must look like
Published assumptions, not our results. The four Assumes lines do not overlap, which is why the exploratory analysis has to come first.
PC [1]
baseline, not one of the three
RETURNS
a CPDAG over the 31 variables, no lags
ASSUMES
i.i.d. samples and an invertible covariance
ORIENTS BY
v-structures, then Meek's rules
BUILT ON
tigramite PC-stable, majority colliders [6]
PCMCI+ [2]
announced method
RETURNS
lagged + contemporaneous graph, then a summary
ASSUMES
stationarity; autocorrelation is modelled
ORIENTS BY
time order for lags, CI rules for the rest
BUILT ON
tigramite with the ParCorr test [6]
VAR-LiNGAM [3]
announced method
RETURNS
VAR coefficients plus contemporaneous B0
ASSUMES
VAR residuals that are non-Gaussian
ORIENTS BY
ICA; the non-Gaussian contrast fixes B0
BUILT ON
lingam, adaptive lasso with a bootstrap [7]
LSTE [4,5]
announced method
RETURNS
one TE test per source, target and lag
ASSUMES
stationarity; enough samples for a kNN density
ORIENTS BY
time order alone: source precedes target
BUILT ON
tigramite CMIknn + shuffle test, BH [6,9]
[1] Spirtes & Glymour, Social Science Computer Review 9(1), 1991 - PC [2] Runge, UAI 2020 - PCMCI+ [3] Hyvarinen, Zhang, Shimizu & Hoyer, JMLR 11, 2010 - VAR-LiNGAM [4] Schreiber, Phys. Rev. Lett. 85(2), 2000 - transfer entropy [5] Kraskov, Stogbauer & Grassberger, Phys. Rev. E 69:066138, 2004 [6] tigramite 5.2.10.1 - github.com/jakobrunge/tigramite [7] lingam 1.13.0 - github.com/cdt15/lingam [9] Benjamini & Hochberg, JRSS-B 57(1), 1995 - FDR
Notes: The point of this table is column three. The four assumptions are different and non-overlapping, which is what makes the next slide necessary.

## Slide 4
OUR MEASUREMENT
4
What the EDA measured: every assumption but one is violated
Seven assumptions, measured on the data before any algorithm ran. One row is good news.
ASSUMPTION
WHAT WE MEASURED ON THIS DATASET
PC
PCMCI+
VAR-LiNGAM
LSTE
violated
satisfied
not assumed
Independent samples
lag-1 autocorrelation up to 0.981; Ljung-Box rejects 27 of 31
Stationarity
ADF calls 30 of 31 stationary, KPSS only 24; the two disagree on 8
Non-Gaussian VAR residuals
mean |excess kurtosis| 0.141 vs a threshold of 1.0; 0 of 31 clear it
Adequate sample size
binding effective n is 36 of 1499 rows - 2.4% of the nominal count
Well-conditioned covariance
condition number 3388 vs a threshold of 1000; 9 variables VIF > 10
Linearity
0 of 465 pairs have distance correlation exceeding |Pearson| by 0.1
Causal sufficiency
X27 and X31 are in the truth but absent from the data; 4 edges lost
EDA verdict
the EDA's own outlook, recorded before any run
fails
fails
fails
works, with
caveats
Only linearity holds, and it holds cleanly - which is why every method here uses its linear or partial-correlation test rather than a nonlinear one. Everything else in this matrix is a prediction of failure, and slide 7 checks each one against what actually happened.
Notes: This is the slide the rest of the deck hangs off. Every mark is from the EDA report's own per-algorithm verdict. Note the one clean row - linearity - which is why we use ParCorr and not GPDC.

## Slide 5
EXPERIMENTAL SETUP
5
Experimental setup: every parameter read off the EDA, not chosen
Where a value could have been a preference, the slide names the measurement that fixed it instead
DATA AND PREPROCESSING
Dataset
datasetTE.csv - 1499 rows x 31 variables [8,10]
Standardised
yes; largest / smallest column SD = 2525x, so an unscaled
kernel or distance would be dominated by one variable
Ground truth
33-node DAG, 32 edges -> projected onto the 31 observed
variables, giving the 30-edge primary target
Integrity
0 missing values, 0 duplicate rows, no constant or
near-constant columns; a regular 1-unit sampling interval
PARAMETERS, AND WHERE EACH CAME FROM
tau_max
swept over 1, 2, 3 - the VAR order criteria disagree
(AIC 3, BIC 1, HQIC 2, FPE 3), so none was privileged
alpha
0.01 for PC and PCMCI+ (Fisher-z / ParCorr); 0.05 for
LSTE, then Benjamini-Hochberg over its 2790 tests [9]
VAR-LiNGAM
adaptive lasso, pruning on, 10 bootstrap resamples,
criterion: bic - which overrode the tau we asked for
LSTE
CMIknn, k = 0.1n, 20-shuffle significance test [5,6]
SCORING
Primary target
gt_projected, 30 edges. Also scored against the induced
subgraph and against both targets' CPDAGs
Baselines
empty graph = SHD 30. The truth's CPDAG leaves 6 edges
undirectable by any observational method
Prior knowledge
4 edges, direction taken from the ground truth file.
An oracle and a best case - not independent validation
The prior-knowledge rows are the one place a result could flatter itself, so they are labelled as an oracle everywhere they appear - including on the results chart.
[5] Kraskov, Stogbauer & Grassberger, Phys. Rev. E 69:066138, 2004 [6] tigramite 5.2.10.1 - github.com/jakobrunge/tigramite [8] Menghi et al., arXiv:2208.01529, 2022 - CIPCaD-Bench [9] Benjamini & Hochberg, JRSS-B 57(1), 1995 - FDR [10] Downs & Vogel, Computers & Chemical Engineering 17(3), 1993 - TE
Notes: Nothing here was chosen by preference. tau is swept because the four order criteria disagree; standardisation is on because of the 2525x scale ratio. The prior knowledge is an oracle and we say so.

## Slide 6
OUR RESULTS
6
Measured results: the SHD ranking and recovery ranking disagree
Ranked by SHD, the best method predicts nothing at all. That is a fact about SHD, so both panels are shown.
STRUCTURAL HAMMING DISTANCE - LOWER IS BETTER
0
50
100
150
200
empty-graph baseline = 30.0
LSTE
tau 3
30.0
0 edges predicted - identical to the empty graph | TP 0 FP 0 FN 30
PC
best of 3; 47.5-48.5
47.5
35 edges; best is pc with prior knowledge | TP 4 FP 23 FN 18
PCMCI+
best of 6
57.0
52 edges; across tau: 57.0 / 66.0 / 61.0 | TP 8 FP 36 FN 14
VAR-LiNGAM
all 6
198.5
195 edges; every configuration scored identically | TP 0 FP 176 FN 11
whiskers span tau = 1, 2, 3
TRUE POSITIVES, OF 30 RECOVERABLE EDGES
PCMCI+
8
tau 1, with prior knowledge
PC
4
pc with prior knowledge; also pc_manual
VAR-LiNGAM
0
195 edges, none of them right
LSTE
0
no edges to be right about
full bar = all 30 edges recovered
Left: SHD against the 30-edge projected target, lower is better. Right: true positives out of the 30 recoverable edges. The two panels rank the methods differently, and the right one is the one that answers whether we recovered the graph.
Notes: Two panels because the two orderings disagree. LSTE is first on SHD and last on recovery. If you only show the left panel you have published a lie.

## Slide 7
ANALYSIS
7
Predicting more edges is not recovering more edges
Edges predicted against edges recovered. The diagonal is the ceiling; every method sits far below it.
EDGES PREDICTED AGAINST EDGES RECOVERED
0
10
20
30
0
50
100
150
200
true positives
edges predicted
ceiling: true positives <= min(edges, 30)
the truth: 30 of 30
LSTE (0, 0)
PC (35, 4)
PCMCI+ (52, 8)
VAR-LiNGAM (195, 0)
WHAT THE EDA SAID, AND WHAT WE FOUND
VAR-LiNGAM
prediction held
195 edges, none of them right. Two causes: tau never reached the library, and Gaussian residuals leave B0 unidentified.
PCMCI+
prediction held
The most recovery of the four, and the false positives that come with modelling the lag structure.
PC
held, yet ranked first
Fewer edges predicted, so fewer errors charged. Recall of 7-13% is a scoring artefact, not recovery.
LSTE
missed, in the other direction
Sits on the origin. 548 of 2790 tests were significant; BH correction rejected none of them.
Prior knowledge is worth 1.0-1.5 SHD wherever it applies, and nothing at all for VAR-LiNGAM. The ground truth is acyclic with no reciprocal pairs, so the controller-loop structure the prior encodes cannot be scored on this dataset at all.
Notes: Row by row: the EDA prediction, then what happened. Three held. Two things to say out loud: LSTE failed in the direction we were not watching, and VAR-LiNGAM's six identical scores turned out to have a config cause on top of the statistical one - criterion: bic made lingam ignore the tau we swept.

## Slide 8
OUR RESULTS
8
Why LSTE and VAR-LiNGAM were not run exhaustively: runtime
Coverage is not uniform across the four methods, because the runtimes are not within two orders of magnitude of each other.
RUNTIME PER CONFIGURATION, LOG SCALE
1 s
10 s
100 s
1000 s
PC
2.7
per configuration
PCMCI+
32.6
slowest configuration, tau = 3
VAR-LiNGAM
120.7
tau = 1, with the lag-0 bootstrap
LSTE
1434.2
a single configuration, tau = 3
358 s
all 15 PC, PCMCI+ and VAR-LiNGAM runs
1434 s
one LSTE configuration
4.0x
one LSTE cell costs 4x the rest of the grid
WHICH CELLS OF THE GRID WERE RUN
t1
t1+PK
t2
t2+PK
t3
t3+PK
PC
3 runs incl. the pc_manual oracle - tau does not apply
PCMCI+
6 of 6
VAR-LiNGAM
6 of 6, but the lag-0 bootstrap only at tau = 1
LSTE
1 of 6
run and scored
not run
does not apply
+ bootstrap
The LSTE and VAR-LiNGAM conclusions therefore rest on less evidence than the PCMCI+ ones. LSTE ran at tau = 3 only with no prior-knowledge variant; VAR-LiNGAM's bootstrap ran at tau = 1 only, at 10 resamples. Both gaps are cost, not choice.
Notes: Say this one plainly: LSTE and VAR-LiNGAM are under-covered, and it is because of runtime. One LSTE cell costs four times the whole rest of the grid.

## Slide 9
OUR LEARNING
9
Key learnings from the experiments
What we would carry into the next dataset, in the order we would apply it.
01
The EDA earned its place, and its one miss is the useful part.
It called VAR-LiNGAM, PCMCI+ and PC correctly before a single run. It missed LSTE by sizing the estimator's power and not the correction stacked on top of it.
02
An identical score in every cell means a knob was not connected.
VAR-LiNGAM returned SHD 198.5 six times. With criterion: bic set, lingam picks its own lag order and ignores the tau we asked for, so the sweep refitted one VAR(1) six times.
03
SHD alone ranks the empty graph first, so baselines are not optional.
The empty graph scores 30.0 and 6 edges of the truth's CPDAG cannot be oriented by any observational method. Both belong on the chart, not in a footnote.
04
A shuffle test has a p-value floor, and it is checkable before the run.
20 shuffles cannot produce a p below 1/21, and BH over 2790 tests will not reject at that floor. Pure arithmetic, now a pre-flight guard rather than 24 minutes of compute.
05
An edge needs a selection rule, not just a non-zero coefficient.
The adaptive lasso left coefficients as small as |b| = 0.0003 on standardised data, and every one became an edge. Selection now goes by bootstrap frequency.
06
The failures are in the data, not in the wrappers we wrote.
On the suite's synthetic case - Laplace innovations, independent samples - the same code recovers the generating graph. Nothing here is a broken wrapper.
The first four transfer to any dataset. The last two are about this codebase, and both are already fixed in the working tree.
Notes: The four transferable ones are the first four. The pre-flight feasibility check is the one that would have saved actual time.

## Slide 10
CONCLUSION
10
Conclusion, and the one next step that matters
Two of the three next steps are cheap. The third is the only one that changes an outcome.
What we did
Implemented and ran PCMCI+, VAR-LiNGAM and LSTE on Tennessee Eastman, with PC as an i.i.d. baseline.
16 scored configurations, every assumption measured first and every violation recorded with its number.
What we found
No method beats the empty-graph baseline in a way that means anything: the best recall is 8 of 30 edges.
Each failure traces to a quantity measured before the run - Gaussian residuals, effective n of 36, a condition number of 3388.
What it cost us to learn
A 24-minute LSTE run that could not have produced an edge at any significance level.
A six-cell VAR-LiNGAM grid that refitted the same VAR(1) six times, because a config key overrode the lag order we swept.
NEXT
Re-run the two fixed methods
coded, not yet run
LSTE with more shuffles or FDR off; VAR-LiNGAM with bootstrap selection
Close the coverage gaps
cost-bound
LSTE across tau 1-3 and with prior knowledge; the bootstrap at every tau
Attack the binding constraint
the real one
Effective n of 36 defeats everything here; a longer segment beats tuning
UNVERIFIED - the two fixes above are in the working tree, not in the run this deck reports. No number on any earlier slide comes from them.
The headline is not that four methods failed, but that we could say which would fail, and why, before running them.
Notes: The fixes are written but not run. Nothing on the results slides depends on them, and we should not present them as results.