## Slide 1
ROOT-CAUSE DETECTION · BENCHMARK RESULTS
Causal discovery on the quadruple-tank process: raw data versus Gaussian-copula-transformed data
PC, PCMCI+, VAR-LiNGAM and LSTE on datasets P_minus and P_plus.
Results produced on 2 October 2026.
Runs: run-parcorr-tau20-s3, run-parcorr-tau20-full, run-copula-tau20-s3, run-copula-tau20-full, run-copula-lste-s3

## Slide 2
THE SYSTEM
Two pumps, four tanks, one disturbance: eight directed links are the answer key for every result that follows
Source: datasets/QTank_Dynamics.m; Johansson, IEEE TCST 2000; datasets/generated/ground_truth_edges.json
2
Physical rig (Johansson quadruple-tank process)
h3
upper left
h4
upper right
h1
lower left
h2
lower right
d
pump v1
pump v2
Each pump splits its flow between one lower tank and the diagonally opposite upper tank. Upper tanks drain into the tank below (burgundy). d feeds both upper tanks.
Same system as a causal graph: 7 nodes, 8 directed links
v1
d
v2
h3
h4
h1
h2
Variable | Meaning | Type
v1, v2 | pump voltages | binary PRBS inputs
d | disturbance flow into upper tanks | binary PRBS input
h1, h2 | lower-tank levels | continuous
h3, h4 | upper-tank levels | continuous

## Slide 3
DATA AND SETUP
Two operating points, two sampling rates, one window of 20 lags; every run is scored against the same 8 edges
Source: datasets/generated/ground_truth_edges.json; datasets/run_algorithms.py; docs/QTP_EXPECTATIONS.md
3
Benchmark settings
Item | Value
Datasets | P_minus (minimum phase), P_plus (non-minimum phase); same simulator and inputs
Variables | v1, v2, d (binary PRBS inputs); h1, h2, h3, h4 (tank levels)
Ground truth | 8 directed edges; no lag information recorded
Sampling, full | Ts = 5 s, 2880 rows (4 h)
Sampling, stride 3 | Ts = 15 s, 960 rows (same 4 h)
tau_max | 20 samples = 100 s (full) or 300 s (stride 3)
Standardisation | every column z-scored before each algorithm
Scoring | lags collapsed to unique directed edges; self-loops dropped; precision, recall, F1, SHD
Ground-truth edges
cause → effect
# | Cause | Effect | Mechanism
1 | v1 | h1 | pump flow
2 | v1 | h4 | pump flow
3 | v2 | h2 | pump flow
4 | v2 | h3 | pump flow
5 | d | h3 | disturbance
6 | d | h4 | disturbance
7 | h3 | h1 | drainage
8 | h4 | h2 | drainage

## Slide 4
DATA AND SETUP · INPUT AND NOISE SIGNALS
Three binary excitations drive the plant and two small Gaussian noises perturb it; only the three excitations are recorded as inputs
Source: datasets/generate_qtank_data.py (QTankParams, prbs, simulate); datasets/generated/*_meta.json; Johansson, IEEE TCST 2000 (Q_mat, R_mat)
4
The five signals
amplitudes as generated, seed 0
Signal | Role | Type | Amplitude | Hold / rate | Recorded | Enters
v1 | pump 1 excitation | PRBS, ± | ±0.30 V around 3.00 V (P−) / 3.15 V (P+) | 30 s = 6 samples | yes, as v1 | h1 (gam1), h4 (1−gam1)
v2 | pump 2 excitation | PRBS, ± | ±0.30 V around 3.00 V (P−) / 3.15 V (P+) | 30 s = 6 samples | yes, as v2 | h2 (gam2), h3 (1−gam2)
d | disturbance flow | PRBS, ± | ±0.50 flow units, zero mean | 50 s = 10 samples | yes, as d | h3 (0.40), h4 (0.60)
pump noise | actuator error | Gaussian, white | sd 0.05 V (R_mat) | every 5 s sample | no | applied voltage, both pumps
meas. noise | sensor error | Gaussian, white | sd 0.05 cm (Q_mat) | every 5 s sample | inside h1–h4 | recorded levels only
First 10 minutes of the recorded inputs
P_minus, Ts 5 s, zero-order hold
v1 [V]
v2 [V]
d [flow]
0 s 300 s 600 s
Design choices and why
– Why PRBS and not Gaussian excitation: the reference identification experiment used binary sequences, and VAR-LiNGAM needs non-Gaussian inputs to orient edges (PRBS excess kurtosis ≈ −2). For PC and PCMCI+ a held Gaussian of equal variance would work about as well.
– Why a 30 s hold: one third of the dominant time constant (about 90 s), so each switch is seen by the tanks while the run still contains about 480 switches.
– Why d holds for 50 s: different from the pumps so the three inputs never synchronise and their effects separate at every lag.
– Why ±0.30 V: keeps levels within a few cm of the operating point, where the square-root outflow is close to linear.
– Why the pump noise is unrecorded: the CSV stores the command, the plant sees command plus noise, so v1 and v2 stay exactly binary and the noise acts as process noise on the levels.
– Why sd 0.05 on both noises: the values of Q_mat and R_mat in the original Matlab model; six times smaller than the excitation.
– Steady states: P− levels (12.4, 12.7, 1.8, 1.4) cm, P+ levels (12.6, 13.0, 4.8, 4.9) cm. Burn-in of 600 s discarded before recording. 2880 rows kept.
– Consequence: the three input columns can never pass a normality test, before or after any marginal transform.

## Slide 5
ALGORITHMS
Four algorithms with identical settings on raw and transformed data; LSTE is restricted to 8 lags by cost
Source: datasets/run_algorithms.py (CONFIGS); run_summary.json of each run
5
Configuration
Algorithm | Type | Independence test / estimator | Settings | Runs in this deck
PC (lagged, PC-stable) | constraint-based | ParCorr | pc_alpha 0.01, tau_max 20 | raw + copula, 960 and 2880 rows
PCMCI+ | constraint-based, autocorrelation-aware | ParCorr | pc_alpha 0.01, tau_max 20 | raw + copula, 960 and 2880 rows
VAR-LiNGAM | functional (non-Gaussian ICA) | none; VAR + ICA | lags 20, bootstrap 100, edge threshold 0.9 | raw + copula, 960 and 2880 rows
LSTE | information-theoretic | CMIknn, shuffle test | tau_max 8, 100 shuffles, alpha 0.05, FDR BH | copula, 960 rows, P_minus only
– ParCorr assumes linear dependence with Gaussian residuals; the copula transform targets the second assumption.
– LSTE at tau_max 20 was not run: 980 CMIknn tests per dataset at that window did not finish in earlier attempts. Cost at tau 20 is UNVERIFIED.
– The raw-data LSTE reference (run-lste-quick) returned 0 edges; its runtime was not recorded.

## Slide 6
DATA PREPROCESSING · 1 OF 3
The copula transform maps each tank level to a near-Gaussian marginal; the three binary inputs stay two-valued
Source: src/causal_bench/eda/copula.py; results/eda-20261002-072603/figures (P_minus, 2880 rows)
6
Before: raw marginals
P_minus, 2880 rows
After: per-column Gaussian copula
same rows
– Transform: QuantileTransformer(output_distribution="normal"), one transformer per column, n_quantiles = sample size. Dependence between columns is left unchanged.
– v1, v2, d are PRBS inputs with two values; they map to two normal quantiles and remain two-valued. No marginal transform makes a two-valued column continuous.

## Slide 7
DATA PREPROCESSING · 2 OF 3
Formal normality tests still reject on most columns after the transform; only Anderson-Darling rejections fall, from 7 to 3
Source: results/eda-20261002-072603/eda_summary.json (P_minus); results/eda-20261002-072543/eda_summary.json (P_plus); alpha 0.05
7
Columns rejected by each normality test (of 7)
P_minus, before vs after
Chart: columns rejected
| Shapiro-Wilk | D'Agostino K² | Jarque-Bera | Anderson-Darling
before | 7 | 6 | 6 | 7
after | 7 | 7 | 7 | 3
Both datasets
rejections of 7 columns
Test | P− before | P− after | P+ before | P+ after
Shapiro-Wilk | 7 | 7 | 7 | 7
D'Agostino K² | 6 | 7 | 7 | 7
Jarque-Bera | 6 | 7 | 6 | 7
Anderson-Darling | 7 | 3 | 7 | 3
Practically Gaussian* | 4 | 4 | 4 | 4
* |skew| < 0.5 and |excess kurtosis| < 1. Counts the four tank levels before and after.
– At n = 2880 the formal tests reject on departures too small to matter; the effect-size row is the operative one.
– The three binary inputs fail every test before and after, as expected.

## Slide 8
DATA PREPROCESSING · 3 OF 3
No MAD outliers in either dataset; after the transform 3 to 4 percent of rows exceed the Hotelling T² control limit, against 5 percent expected
Source: results/eda-20261002-072603/figures/step4_t2_control_chart.png; eda_summary.json of both EDA runs
8
Hotelling T² per observation after the transform
P_minus; UCL at alpha 0.05
Outliers and T² exceedance
Measure | P_minus | P_plus
MAD outliers (¦z¦ > 3.5) | 0 | 0
IQR outliers (1.5 IQR) | 22 | 46
T² UCL | 14.12 | 14.12
Fraction above UCL | 0.028 | 0.042
Expected under null | 0.050 | 0.050
– Nothing is removed: outlier counts are diagnostic only, so the time index stays intact.
– The exceedance fraction below 0.05 is consistent with a successful marginal transform; it says nothing about causal structure.

## Slide 9
RESULTS ON RAW DATA
PCMCI+ scores highest on both datasets at both row counts; stride 3 beats the full series for every algorithm
Source: results/qtank/run-parcorr-tau20-s3/scores.json; run-parcorr-tau20-full/scores.json
9
F1 against the 8 true edges
raw data
Chart: 
| PC | PCMCI+ | VAR-LiNGAM
P_minus, 960 rows | 0.6667 | 0.875 | 0.6667
P_plus, 960 rows | 0.7692 | 0.8889 | 0.8889
P_minus, 2880 rows | 0.5714 | 0.8235 | 0.6316
P_plus, 2880 rows | 0.5455 | 0.8235 | 0.7619
All scores
raw data
Rows | Dataset | Algorithm | Prec. | Recall | F1 | SHD
960 | P_minus | PC | 0.71 | 0.62 | 0.67 | 6
960 | P_minus | PCMCI+ | 0.88 | 0.88 | 0.88 | 2
960 | P_minus | VAR-LiNGAM | 0.60 | 0.75 | 0.67 | 5
960 | P_plus | PC | 1.00 | 0.62 | 0.77 | 3
960 | P_plus | PCMCI+ | 0.80 | 1.00 | 0.89 | 2
960 | P_plus | VAR-LiNGAM | 0.80 | 1.00 | 0.89 | 2
2880 | P_minus | PC | 0.67 | 0.50 | 0.57 | 6
2880 | P_minus | PCMCI+ | 0.78 | 0.88 | 0.82 | 3
2880 | P_minus | VAR-LiNGAM | 0.55 | 0.75 | 0.63 | 8
2880 | P_plus | PC | 1.00 | 0.38 | 0.55 | 5
2880 | P_plus | PCMCI+ | 0.78 | 0.88 | 0.82 | 2
2880 | P_plus | VAR-LiNGAM | 0.62 | 1.00 | 0.76 | 5
– PC has the lowest recall everywhere (0.38 to 0.62): it finds the pump links and misses the drainage links.
– The denser 5 s series lowers F1 for PC and VAR-LiNGAM; a 20-lag window then spans only 100 s against a 90 s time constant.

## Slide 10
RESULTS AFTER THE COPULA TRANSFORM
The transform moves F1 by at most 0.10 in either direction and leaves the ranking unchanged
Source: results/qtank/COPULA_RESULTS.md; run-copula-tau20-s3, run-copula-tau20-full, run-copula-lste-s3
10
F1, raw vs copula
960 rows (left pair) and 2880 rows (right pair) per algorithm
Chart: 
| PC P_minus 960 | PCMCI+ P_minus 960 | VAR-LiNGAM P_minus 960 | PC P_plus 960 | PCMCI+ P_plus 960 | VAR-LiNGAM P_plus 960 | PC P_minus 2880 | PCMCI+ P_minus 2880 | VAR-LiNGAM P_minus 2880 | PC P_plus 2880 | PCMCI+ P_plus 2880 | VAR-LiNGAM P_plus 2880
raw | 0.6667 | 0.875 | 0.6667 | 0.7692 | 0.8889 | 0.8889 | 0.5714 | 0.8235 | 0.6316 | 0.5455 | 0.8235 | 0.7619
copula | 0.7143 | 0.8571 | 0.6316 | 0.7692 | 0.8235 | 0.8 | 0.6667 | 0.7778 | 0.7059 | 0.6154 | 0.8235 | 0.7368
Change raw → copula
Rows | Dataset | Algorithm | F1 raw | F1 cop. | ΔF1 | SHD raw | SHD cop.
960 | P_minus | PC | 0.67 | 0.71 | +0.05 | 6 | 5
960 | P_minus | PCMCI+ | 0.88 | 0.86 | -0.02 | 2 | 2
960 | P_minus | VAR-LiNGAM | 0.67 | 0.63 | -0.04 | 5 | 8
960 | P_plus | PC | 0.77 | 0.77 | +0.00 | 3 | 3
960 | P_plus | PCMCI+ | 0.89 | 0.82 | -0.07 | 2 | 2
960 | P_plus | VAR-LiNGAM | 0.89 | 0.80 | -0.09 | 2 | 5
2880 | P_minus | PC | 0.57 | 0.67 | +0.10 | 6 | 4
2880 | P_minus | PCMCI+ | 0.82 | 0.78 | -0.05 | 3 | 4
2880 | P_minus | VAR-LiNGAM | 0.63 | 0.71 | +0.07 | 8 | 5
2880 | P_plus | PC | 0.55 | 0.62 | +0.07 | 5 | 5
2880 | P_plus | PCMCI+ | 0.82 | 0.82 | +0.00 | 2 | 3
2880 | P_plus | VAR-LiNGAM | 0.76 | 0.74 | -0.03 | 5 | 6
960 | P_minus | LSTE | 0.00 | 0.00 | +0.00 | 8 | 8
– PC: F1 unchanged or higher in all four cases (+0.04, 0.00, +0.10, +0.07); false positives fall on P_minus.
– PCMCI+: within 0.07 of raw in every case; SHD unchanged or +1. VAR-LiNGAM: mixed, from −0.09 to +0.08.
– LSTE on copula P_minus: 0 edges in 1313 s. P_plus was not run.

## Slide 11
RECOVERED GRAPHS · PC · P_MINUS (MINIMUM PHASE)
PC on P_minus: F1 rises from 0.67 to 0.71 after the transform
Source: directed_edges in results/qtank/run-parcorr-tau20-s3/graphs and run-copula-tau20-s3/graphs, lags collapsed; scores.json of both runs; 960 rows, tau_max 20
11
Found (true link recovered)
Invented (not in ground truth)
Reversed (true link, wrong direction)
Missed (true link not found)
Ground truth
8 links
v1
d
v2
h3
h4
h1
h2
PC, raw data
F1 0.67 · SHD 6
v1
d
v2
h3
h4
h1
h2
found 5 · invented 2 · reversed 1 · missed 3
PC, copula-transformed
F1 0.71 · SHD 5
v1
d
v2
h3
h4
h1
h2
found 5 · invented 1 · reversed 1 · missed 3
Change raw → copula. True links gained: none. True links lost: none. Wrong links added: none. Wrong links removed: h1→h2.

## Slide 12
RECOVERED GRAPHS · PC · P_PLUS (NON-MINIMUM PHASE)
PC on P_plus: F1 unchanged at 0.77 after the transform
Source: directed_edges in results/qtank/run-parcorr-tau20-s3/graphs and run-copula-tau20-s3/graphs, lags collapsed; scores.json of both runs; 960 rows, tau_max 20
12
Found (true link recovered)
Invented (not in ground truth)
Reversed (true link, wrong direction)
Missed (true link not found)
Ground truth
8 links
v1
d
v2
h3
h4
h1
h2
PC, raw data
F1 0.77 · SHD 3
v1
d
v2
h3
h4
h1
h2
found 5 · invented 0 · reversed 0 · missed 3
PC, copula-transformed
F1 0.77 · SHD 3
v1
d
v2
h3
h4
h1
h2
found 5 · invented 0 · reversed 0 · missed 3
Change raw → copula. True links gained: none. True links lost: none. Wrong links added: none. Wrong links removed: none.

## Slide 13
RECOVERED GRAPHS · PCMCI+ · P_MINUS (MINIMUM PHASE)
PCMCI+ on P_minus: F1 falls from 0.88 to 0.86 after the transform
Source: directed_edges in results/qtank/run-parcorr-tau20-s3/graphs and run-copula-tau20-s3/graphs, lags collapsed; scores.json of both runs; 960 rows, tau_max 20
13
Found (true link recovered)
Invented (not in ground truth)
Reversed (true link, wrong direction)
Missed (true link not found)
Ground truth
8 links
v1
d
v2
h3
h4
h1
h2
PCMCI+, raw data
F1 0.88 · SHD 2
v1
d
v2
h3
h4
h1
h2
found 7 · invented 0 · reversed 0 · missed 1
PCMCI+, copula-transformed
F1 0.86 · SHD 2
v1
d
v2
h3
h4
h1
h2
found 6 · invented 0 · reversed 0 · missed 2
Change raw → copula. True links gained: none. True links lost: h4→h2. Wrong links added: none. Wrong links removed: none.

## Slide 14
RECOVERED GRAPHS · PCMCI+ · P_PLUS (NON-MINIMUM PHASE)
PCMCI+ on P_plus: F1 falls from 0.89 to 0.82 after the transform
Source: directed_edges in results/qtank/run-parcorr-tau20-s3/graphs and run-copula-tau20-s3/graphs, lags collapsed; scores.json of both runs; 960 rows, tau_max 20
14
Found (true link recovered)
Invented (not in ground truth)
Reversed (true link, wrong direction)
Missed (true link not found)
Ground truth
8 links
v1
d
v2
h3
h4
h1
h2
PCMCI+, raw data
F1 0.89 · SHD 2
v1
d
v2
h3
h4
h1
h2
found 8 · invented 2 · reversed 0 · missed 0
PCMCI+, copula-transformed
F1 0.82 · SHD 2
v1
d
v2
h3
h4
h1
h2
found 7 · invented 1 · reversed 1 · missed 1
Change raw → copula. True links gained: none. True links lost: h4→h2. Wrong links added: h2→h4. Wrong links removed: h4→h1.

## Slide 15
RECOVERED GRAPHS · VAR-LINGAM · P_MINUS (MINIMUM PHASE)
VAR-LiNGAM on P_minus: F1 falls from 0.67 to 0.63 after the transform
Source: directed_edges in results/qtank/run-parcorr-tau20-s3/graphs and run-copula-tau20-s3/graphs, lags collapsed; scores.json of both runs; 960 rows, tau_max 20
15
Found (true link recovered)
Invented (not in ground truth)
Reversed (true link, wrong direction)
Missed (true link not found)
Ground truth
8 links
v1
d
v2
h3
h4
h1
h2
VAR-LiNGAM, raw data
F1 0.67 · SHD 5
v1
d
v2
h3
h4
h1
h2
found 6 · invented 3 · reversed 1 · missed 2
VAR-LiNGAM, copula-transformed
F1 0.63 · SHD 8
v1
d
v2
h3
h4
h1
h2
found 6 · invented 6 · reversed 0 · missed 2
Change raw → copula. True links gained: none. True links lost: none. Wrong links added: h1→h2, h4→h1, v2→h4. Wrong links removed: h1→h3.

## Slide 16
RECOVERED GRAPHS · VAR-LINGAM · P_PLUS (NON-MINIMUM PHASE)
VAR-LiNGAM on P_plus: F1 falls from 0.89 to 0.80 after the transform
Source: directed_edges in results/qtank/run-parcorr-tau20-s3/graphs and run-copula-tau20-s3/graphs, lags collapsed; scores.json of both runs; 960 rows, tau_max 20
16
Found (true link recovered)
Invented (not in ground truth)
Reversed (true link, wrong direction)
Missed (true link not found)
Ground truth
8 links
v1
d
v2
h3
h4
h1
h2
VAR-LiNGAM, raw data
F1 0.89 · SHD 2
v1
d
v2
h3
h4
h1
h2
found 8 · invented 2 · reversed 0 · missed 0
VAR-LiNGAM, copula-transformed
F1 0.80 · SHD 5
v1
d
v2
h3
h4
h1
h2
found 8 · invented 5 · reversed 0 · missed 0
Change raw → copula. True links gained: none. True links lost: none. Wrong links added: h1→h2, h2→h1, h3→h2, h4→h1. Wrong links removed: v1→h2.

## Slide 17
TIGRAMITE NATIVE PLOTTING
tigramite.plotting draws one graph adequately and does not cover comparison, scoring or long windows
Source: results/qtank/tigramite-plots-run-copula-tau20-s3/README.md and status.md; datasets/tigramite_plots.py
17
plot_graph
PCMCI+, copula P_minus
plot_time_series_graph
same graph, 21 lag columns
Edge colour MCI, node colour auto-MCI, lag labels on edges.
21 lag columns × 7 variables; every repeated lag drawn.
What was tried and what broke
10 functions, 58 files
– All 10 plotting functions ran on the saved graphs after conversion to tigramite's (N, N, tau+1) string array.
– plot_time_series_graph and plot_tsg are unreadable at tau_max 20; usable only up to about 5 lags.
– Node colour in plot_graph is auto-MCI, which has no meaning for VAR-LiNGAM graphs.
– Mediation plots need a fitted LinearMediation model, drop contemporaneous links, and label the path np.int64(1) under NumPy 2.
– No multi-algorithm comparison, no ground-truth overlay, no precision/recall/SHD plots.
– plot_densityplots imports seaborn, which is not a declared dependency.
– Ground truth cannot be drawn at lag 0 without mirrored reverse links; it was drawn at lag 1.
– Verdict: use tigramite plots for a single PCMCI+ result at short windows; keep the comparison figures in this deck native or matplotlib.

## Slide 18
RUNTIME
The copula transform roughly doubles VAR-LiNGAM runtime; PC and PCMCI+ stay under one minute in every configuration
Source: run_summary.json of run-parcorr-tau20-s3, run-parcorr-tau20-full, run-copula-tau20-s3, run-copula-tau20-full, run-copula-lste-s3
18
Wall-clock seconds per algorithm and dataset
log scale
Chart: 
| PC P_minus 960 | PCMCI+ P_minus 960 | VAR-LiNGAM P_minus 960 | PC P_plus 960 | PCMCI+ P_plus 960 | VAR-LiNGAM P_plus 960 | PC P_minus 2880 | PCMCI+ P_minus 2880 | VAR-LiNGAM P_minus 2880 | PC P_plus 2880 | PCMCI+ P_plus 2880 | VAR-LiNGAM P_plus 2880
raw | 4.4 | 1.2 | 135 | 4.6 | 1.4 | 134.3 | 21.2 | 3.8 | 300.1 | 22.7 | 3.8 | 288.7
copula | 3.4 | 2 | 239.7 | 8.5 | 5.3 | 249.3 | 30.9 | 7.3 | 516.4 | 33.6 | 4.5 | 468.7
Copula / raw ratio
Rows | Dataset | Algorithm | Raw (s) | Copula (s) | Ratio
960 | P_minus | PC | 4.4 | 3.4 | 0.8
960 | P_minus | PCMCI+ | 1.2 | 2.0 | 1.7
960 | P_minus | VAR-LiNGAM | 135.0 | 239.7 | 1.8
960 | P_plus | PC | 4.6 | 8.5 | 1.8
960 | P_plus | PCMCI+ | 1.4 | 5.3 | 3.8
960 | P_plus | VAR-LiNGAM | 134.3 | 249.3 | 1.9
2880 | P_minus | PC | 21.2 | 30.9 | 1.5
2880 | P_minus | PCMCI+ | 3.8 | 7.3 | 1.9
2880 | P_minus | VAR-LiNGAM | 300.1 | 516.4 | 1.7
2880 | P_plus | PC | 22.7 | 33.6 | 1.5
2880 | P_plus | PCMCI+ | 3.8 | 4.5 | 1.2
2880 | P_plus | VAR-LiNGAM | 288.7 | 468.7 | 1.6
960 | P_minus | LSTE | UNVERIFIED | 1313.1 | n/a
The copula runs shared the machine with the LSTE run; the share of the ratio due to contention is UNVERIFIED.

## Slide 19
OPEN ITEMS
Four measurements are missing from this benchmark
Source: Plan.md (2026-09-27); results/qtank/run-lste-quick; results/qtank/run-copula-lste-s3/run_summary.json
19
Not run, not completed, or not recorded
Item | Status | Reason | Cost to close
LSTE on P_plus (copula, tau 8, 100 shuffles) | Not run | Stopped after P_minus on request | about 22 min (P_minus took 1313 s)
LSTE at tau_max 20 | Not run | 980 CMIknn tests per dataset; earlier attempts did not finish | UNVERIFIED
CMIknn test for PC and PCMCI+ (Plan.md) | Not completed | Nonparametric test at 500 shuffles | about 2.7 h for both datasets, UNVERIFIED
LSTE raw-data runtime (run-lste-quick) | Not recorded | Run directory holds graphs only, no run_summary.json | re-run, same cost as above