## Slide 1: The setup — the same reactor, one new assumption
Three sensors on a reactor cooling loop, read once a minute for 300 minutes. Only the noise distribution has changed.
THE THREE SENSORS
F
coolant flow
l/min
T
reactor temperature
°C
P
vessel pressure
bar
HOW THE DATA WAS MADE
F(t) = 0.60 F(t−1) + ε
T(t) = 0.65 T(t−1) + 0.50 F(t−1) + ε
P(t) = 0.80 T(t) + ε
same minute
ε is uniform noise, independent across sensors and across time — not Gaussian. That one change is what VAR-LiNGAM feeds on.
THE FIRST SIX MINUTES OF THE RECORDING
minute
F l/min
T °C
P bar
1
40.69
309.52
11.83
2
39.88
308.72
10.89
3
38.37
308.85
11.91
4
40.17
309.60
11.69
5
39.67
308.63
11.11
6
39.19
308.00
9.03
300 rows in total · 299 usable once one lag is cut off the front
SETTINGS
τmax = 1
one minute of memory covers the true delays
N = 300
rows, estimated by ordinary least squares
excess kurtosis −1.14, −1.09, −0.60
the residuals are flat-topped, far from Gaussian
prune at |b| < 0.05
anything smaller is read as estimation noise
Notes: Same three sensors and the same generating equations as the PCMCI+ half. The only difference is that the shocks are uniform, not Gaussian.

## Slide 2: Two kinds of link, and why one of them needs a new idea
A lagged link is ordered by the clock. A same-minute link is not, so the algorithm has to read the shape of the noise instead.
LAGGED — THE CLOCK DECIDES
t − 1
F
T
P
t
F
T
P
A cause in an earlier minute cannot be the effect of a later one. Nothing has to be tested — the direction is given.
SAME MINUTE — THE CLOCK IS SILENT
T
P
T
P
corr( nT , nP ) = 0.771
One number, two stories. A correlation is symmetric, so least squares alone can never choose between these two arrows.
THE NEW INGREDIENT
one shock
two shocks added together
Adding independent shocks pulls the shape toward a bell. So the direction whose leftover stays un-bell-like, and independent of its predictor, is the one that un-mixed the data.
OUR PAIR
We follow T and P again — the same pair the PCMCI+ half followed, settled here by a completely different argument.
Notes: Motivation slide. The whole algorithm exists because lag-0 links carry no time ordering.

## Slide 3: The model, written down
Two ways to write the same process. A VAR fits the second one, and the algorithm is the trip back to the first.
WHAT THE PROCESS ACTUALLY OBEYS — STRUCTURAL FORM
x(t) = B₀ x(t) + Στ Bτ x(t−τ) + e(t)
B₀ same-minute weights
Bτ lagged weights
e(t) independent, non-Gaussian shocks
WHAT A VAR CAN FIT — REDUCED FORM
x(t) = Στ Mτ x(t−τ) + n(t)
No term on the right is dated t, so this is pure prediction from the past. Everything that happens inside the minute is pushed into the residual n(t).
THE BRIDGE
e(t)
( I − B₀ )⁻¹
n(t)
the VAR residual is a mixture of the true shocks
Mτ = ( I − B₀ )⁻¹ Bτ
Bτ = ( I − B₀ ) Mτ
WHAT MUST BE TRUE
B₀ is acyclic — the same-minute links admit an ordering
the shocks are mutually independent — no hidden common cause
the shocks are non-Gaussian — otherwise the lag-0 order is unidentifiable
the process is stationary over the window
the lag order τmax is large enough to hold the real delays
Notes: The identity B_tau = (I - B0) M_tau is the whole reason the algorithm works. Everything else is estimation.

## Slide 4: The algorithm in four pictures
Fit the past, read the leftovers, order the minute, then undo the mixing. Each stage adds something the one before it could not see.
1 · VAR FIT
t − 1
F
T
P
t
F
T
P
Everything the past can explain, with no same-minute term allowed. P picks up two lagged links it does not really have.
2 · THE RESIDUALS
t − 1
F
T
P
t
F
T
P
nF
nT
nP
What is left is a mixture of the true shocks. The T and P residuals still move together.
3 · LiNGAM ON n(t)
t − 1
F
T
P
t
F
T
P
order F → T → P
Independence picks the same-minute order, and B₀ becomes triangular in it.
4 · CONVERT AND PRUNE
t − 1
F
T
P
t
F
T
P
( I − B₀ ) Mτ removes the contamination, and small weights are dropped.
OUR PAIR
T(t−1) → P(t) appears in picture 1 and is gone by picture 4 — not cut by a test, but cancelled by an identity.
Notes: Overview slide. Panels 1 and 4 are the before and after of the same graph.

## Slide 5: Step 1 — fit the VAR, then look at what is left over
Ordinary least squares, one equation per sensor. The output is a prediction matrix and a residual column for each sensor.
THE PROCEDURE
1
Center every column, then regress x(t) on x(t−1) by ordinary least squares.
2
Collect the coefficients into M₁. This is prediction, not yet structure.
3
Keep the residuals n(t) = x(t) − M₁ x(t−1), one column per sensor.
4
Check that the residuals are non-Gaussian. If they are not, stop — the next step cannot work.
M₁ — WHAT THE PAST PREDICTS
F
T
P
F
T
P
0.572
-0.018
0.001
0.513
0.646
-0.037
0.436
0.553
-0.062
rows = target at t · columns = source at t − 1
Row P says that both F(t−1) and T(t−1) predict pressure. Neither link exists in the equations that made the data. They are the same-minute arrow T(t) → P(t), seen through one lag.
CORRELATION OF THE RESIDUALS
F
T
P
F
T
P
1.000
0.003
0.015
0.003
1.000
0.771
0.015
0.771
1.000
excess kurtosis −1.14 −1.09 −0.60
If the VAR were the whole story these columns would be independent. F is clean, but T and P share 0.771. That leftover dependence is the same-minute link, and it is what step 2 works on.
OUR PAIR
The VAR scores T(t−1) → P(t) at 0.553 and cannot tell that the number is borrowed.
Notes: M1 is a prediction object. Row P carries contamination from the instantaneous link.

## Slide 6: Step 2a — how a direction is decided, drawn once
This one test is the whole of LiNGAM. Regress one residual on another, then ask whether the leftover is independent of what you regressed on.
THE TEST
1
Take the two residual columns and assume a direction, say T causes P.
2
Regress the second residual on the first by least squares and keep the leftover.
3
Measure the dependence between the leftover and the predictor. Zero means independent.
4
Do the same the other way. The direction with the smaller dependence is the cause.
DIRECTION A — T(t) → P(t)
slope = 0.831
leftover (vertical) against predictor (horizontal)
dependence
0.0051
leftover kurtosis
-1.20
An even band. The spread does not change across the plot, and the leftover is still as flat-topped as the original shock.
KEEP
DIRECTION B — P(t) → T(t)
slope = 0.715
leftover (vertical) against predictor (horizontal)
dependence
0.0464
leftover kurtosis
-0.71
Pinched at both ends. The spread depends on the predictor, and the leftover has drifted toward a bell.
REJECT
OUR PAIR
Nine times more dependence the wrong way round. T(t) → P(t) — the same arrow the PCMCI+ half reached through a collider rule.
Notes: Dependence is a normalised HSIC. Zero means independent.

## Slide 7: Step 2b — DirectLiNGAM peels off one sensor per round
A sensor with no same-minute parent leaves no trace in anything it explains. Find it, remove it, repeat.
THE PROCEDURE
1
For each remaining sensor, regress every other one on it and score the worst dependence left behind.
2
The lowest score has no same-minute parent. It goes next in the order.
3
Replace every other column by its leftover after removing that sensor.
4
Repeat on what remains. Then regress each sensor on its predecessors to fill B₀.
ROUND 1
worst dependence as root
F
chosen
0.0030
T
not yet
0.0051
P
not yet
0.0464
P leaves 0.0464 behind in T, so it cannot be first. F and T both sit near zero because no same-minute link joins them, so either may go first.
ROUND 2
worst dependence as root
T
chosen
0.0050
P
not yet
0.0457
After F is removed, P still leaves 0.0457 in T. T is next.
ROUND 3
worst dependence as root
P
chosen
—
Only P is left, so it takes the last place. Order: F → T → P.
OUR PAIR
Regressing on predecessors gives B₀ = 0.831 for T(t) → P(t), with 0.003 and 0.016 everywhere else below the diagonal.
Notes: F and T tie because there is no lag-0 edge between them. Any order with P last yields the same B0.

## Slide 8: Steps 3 and 4 — undo the mixing, then prune
B₀ is known, so the contaminated lagged weights can be corrected in one multiplication.
THE IDENTITY, APPLIED
B₁ = ( I − B₀ ) M₁
1
0
0
−0.003
1
0
−0.016
−0.831
1
·
0.572
-0.018
0.001
0.513
0.646
-0.037
0.436
0.553
-0.062
=
THE ROW THAT MATTERS — PRESSURE
−0.016 × 0.572 − 0.831 × 0.513 + 0.436 = 0.001
−0.016 × −0.018 − 0.831 × 0.646 + 0.553 = 0.016
Both lagged links into pressure collapse to nothing. They were never separate effects — they were T(t) → P(t) counted twice.
AFTER PRUNING AT |b| < 0.05
B₀ same minute
F
T
P
F
T
P
0.000
0.000
0.000
0.003
0.000
0.000
0.016
0.831
0.000
one survivor
0.831
B₁ one minute back
F
T
P
F
T
P
0.572
-0.018
0.001
0.511
0.646
-0.037
0.001
0.016
-0.031
three survivors
0.572 0.511 0.646
green kept · red dropped as estimation noise
OUR PAIR
T(t−1) → P(t) falls from 0.553 to 0.016 and is pruned. PCMCI+ cut it with a conditioning set. Here an identity does it.
Notes: Adaptive lasso or bootstrap thresholds replace the fixed cut-off in production use.

## Slide 9: The recovered graph, and how to read it
Four weighted links, the same four the equations on slide one put in, with the numbers attached.
RECOVERED GRAPH — WEIGHTS ESTIMATED, TRUTH IN BRACKETS
minute t − 1
F
T
P
minute t
F
T
P
0.831
estimated (true)
F(t−1) → F(t)
0.572
(0.60)
F(t−1) → T(t)
0.511
(0.50)
T(t−1) → T(t)
0.646
(0.65)
T(t) → P(t)
0.831
(0.80)
Nothing extra, nothing missing. The same four links the PCMCI+ half recovered, now carrying effect sizes.
HOW TO READ A WEIGHT
A one-unit change in the parent moves the child by b units, with every other parent held fixed. These are structural coefficients, not correlations.
T(t) → P(t) b = 0.831
One degree hotter raises pressure by 0.83 bar inside the same minute. A lag-0 arrow is relative to the sampling interval — read at one second instead, this link would move to lag 1.
WHAT EACH STEP BOUGHT
VAR
everything the past can explain, and clean residuals
LiNGAM
the order inside the minute, and B₀
Convert
lagged weights with the same-minute leak removed
Prune
a graph instead of a dense matrix
WHEN IT BREAKS
residuals close to Gaussian — the lag-0 order stops being identifiable
a hidden common cause — the shocks are no longer independent
τmax too small, or sampling slower than the true delay
Notes: The first failure mode is the live one on the Tennessee Eastman data, where VAR residuals are close to Gaussian.