## Slide 1
ROOT-CAUSE DETECTION · PLANT FLARE DATA
PCA, PC algorithm and T² on the plant flare data: first results
What the pipeline found on 13 months of data from 13 units, how well it worked, and what to fix before the next run.
Run on the lab computer, 22 October 2026
Notes: This deck covers one run: PCA, then the PC algorithm, then T² monitoring, on the real plant data. Every number comes from the output folder of that run.

## Slide 2
SUMMARY
The pipeline works, but the results are not usable yet
Source: pca_pc_t2/outputs/RESULTS.md, tables/ (lab computer run, 22 Oct 2026)
2
99 %
of the time is labelled as flaring
So the 'normal' training data is only 3.8 days long.
2 states
The plant switches between two operating states
The training data contains only one of them. Everything else looks abnormal.
1 tag
One tag explains almost all of the biggest alarm
Tag 99PI3219 in LOUP. It needs a check before we trust the alarm.
WHAT WE NEED NEXT
Three fixes before the next run
1
Build the flare labels again, signal by signal
2
Build a normal baseline that covers both operating states
3
Check tag 99PI3219 for a sensor fault
Notes: Three things stop us from reading the results today. All three can be fixed before the next run.

## Slide 3
WHAT WE RAN
We ran six steps, from raw data to root-cause hypotheses
Source: prompts/CLAUDE_CLI_PROMPT_PCA_PC_T2.md; pca_pc_t2/src; pca_pc_t2/outputs/run.log
3
1 Audit
376 tags found in 13 units (418 expected)
2 Clean
355 tags kept; 581,761 one-minute rows
3 PCA
26 components keep 89% of the variation
4 PC algorithm
Finds links between the 26 components
5 T² and Q
Raises an alarm when the plant moves away from normal
6 Trace
Walks back from an alarm to a candidate unit
How the data was split
Training data: the first 60% of the time, minus the flare windows and 2 hours either side.
Test data: everything else, including all flare windows.
How the run went
All self-checks passed. The run took about 1.5 hours on the lab computer.
Most of that time went to the PC algorithm and its stability check.
Notes: Each step saves its results, so any step can be rerun alone. Each step also checks its own output. All checks passed on the lab computer.

## Slide 4
THE DATA
We used 13 months of one-minute data from 13 units
Source: pca_pc_t2/outputs/00_data_audit.md; tables/missing_by_unit.csv, dropped_tags.csv
4
418 tags expected
376 tags found in the unit folders
42 tags not found. Reason not known yet.
355 tags kept after cleaning
21 dropped: 8 had over 30% missing, 13 never changed
Missing data by unit, before and after cleaning (units above 0.1% only)
NSU_NHT_CCR
8.3% → 5.2%
ISOM_4
8.3% → 8.3%
PG
0.2% → 0.2%
ISOM_3
0.2% → 0.2%
before cleaning
after cleaning
581,761
one-minute rows
13 months
12 Apr 2025 to 21 May 2026
1.1 %
of all values still missing after cleaning. These were filled with the mean.
4
flare signals used to build the flare label
Notes: 42 of the 418 expected tags were not in the unit folders. We have not found out why yet. After cleaning, very little data is missing, except in two units.

## Slide 5
THE FLARE LABEL
The flare label marks 99% of the time as flaring
Source: pca_pc_t2/outputs/00_data_audit.md; tables/flare_detection.csv, flare_thresholds.csv, t2_events.csv
5
Flare label
Training data
T² alarms
Rule: flaring if any of 4 flare signals is above median + 3 × MAD. Gaps of up to 5 samples are joined.
Flare window 1: 82 days
Flare window 2: 318 days
3.8 days in total (0.9% of the data)
One alarm that lasts 404 days
May 2025
Aug 2025
Nov 2025
Feb 2026
May 2026
When almost every minute counts as flaring, the model learns 'normal' from only 3.8 days. The label needs to be built again before the alarm numbers can mean anything. We do not know yet why short spikes join into windows that last months.
Notes: The label is 'flaring' whenever any of the 4 flare signals is above its median plus 3 MAD, with short gaps joined up. It ends up on for 400 of 404 days. That leaves 3.8 days to learn what normal looks like. We have not yet found why the short exceedances join into windows that last months.

## Slide 6
PCA
26 components keep 89% of the variation in the data
Source: pca_pc_t2/outputs/tables/pca_variance.csv, pca_dominant_units.csv
6
0%
25%
50%
75%
100%
1
10
20
30
40
50
60
Number of components
Share of variation kept
26 components: 88.8%
80% needs 11 components
90% needs 30
95% needs 52
99% needs 104
Unit that carries the most weight in each of the 26 components
NSU_NHT_CCR
13
ISOM
4
PDA
4
LOUP
2
PG
2
APS_NVPS_LEU
1
Component 1 is led by LOUP, component 2 by NSU_NHT_CCR and component 3 by ISOM.
Notes: We kept 26 components, as planned. They hold 89% of the variation. For each component we checked which unit's tags carry most of its weight. NSU_NHT_CCR leads half of them.

## Slide 7
A NEW FINDING
The plant switches between two states, and the training data saw only one
Source: pca_pc_t2/outputs/tables/fig09_pc_timeseries.csv (30-minute means; shown here as 6-hour means)
7
0
400
800
1200
May 2025
Aug 2025
Nov 2025
Feb 2026
May 2026
Score of component 2
Gold bands: training data
High state: above 400
38 %
of the time is spent in the high state
14
times the plant moved into the high state
15 Jul 2025
first move, a week after the training data ends
Notes: Component 2 sits near 0 or near 800, with almost nothing in between. That looks like two operating states. The training data comes from April and early July 2025, before the first switch, so it only knows the low state. Please confirm with operations what changes between the two states.

## Slide 8
T² MONITORING
T² stays above its limit almost all the time
Source: pca_pc_t2/outputs/tables/fig15_t2_chart.csv, control_limits.csv, detection_metrics.csv (shown here as 6-hour maxima)
8
1
10
100
1k
10k
100k
1M
10M
100M
99% limit = 46
May 2025
Aug 2025
Nov 2025
Feb 2026
May 2026
Hotelling T², log scale. Gold bands: training data
99.4 %
of test minutes are above the limit
9.2 %
of training minutes are above it too (1% expected)
100 %
of test minutes are above the Q limit
Notes: T² measures how far the plant is from the training data. The limit is 46. On test data it is above the limit 99.4% of the time. The highest plateaus, around 100 million, line up with the high state on the previous slide. Even on the training data it crosses the limit 9% of the time, where 1% is expected.

## Slide 9
WHAT DRIVES THE ALARM
One tag explains almost all of the biggest alarm
Source: pca_pc_t2/outputs/tables/event_peak_tag_contrib.csv, audit_tags.csv, t2_events.csv
9
Share of the peak T² value (92.8 million) by tag, top 10
99PI3219
LOUP
92.8 million
99TI4140
LOUP
29,926
102PI1457B
NSU_NHT_CCR
21,980
71PC9101
DIU
15,745
PPC3501
SEU2
10,722
41TI4124
PDA
7,487
71TC8702
DIU
5,355
102PI4457
NSU_NHT_CCR
4,893
102PC4602R
NSU_NHT_CCR
4,626
41TI41116B
PDA
4,076
≈100 %
of the peak comes from this one tag
0.09 to 169
range of the tag over the year
40 %
of its samples look like outliers
Check this tag with operations: a sensor fault or a real change.
Notes: We split the T² value at its peak into the share from each tag. One LOUP tag accounts for almost all of it. The tag ranges from 0.09 to 169 and looks like an outlier in 40% of samples. Our guess is that it stayed at one level in the training data, so any move looks huge. That guess is not checked yet.

## Slide 10
DETECTION SCORES
The detection scores look good, but they do not mean much yet
Source: pca_pc_t2/outputs/tables/detection_metrics.csv, flare_detection.csv; RESULTS.md
10
What the run reported
Why it does not hold
2 of 2
flares detected
The 2 'flares' are windows of 82 and 318 days. Any alarm will hit them.
2.5 h
median warning before a flare starts
The alarm is on 99.4% of the time, so it is always early.
0.75
AUC for T²
Only 516 non-flare minutes are left to score against, and 70% of them raise an alarm.
Notes: These are the scores the run reported. Each one is a side effect of the flare label covering almost all the time, so none of them tells us how well T² detects flares.

## Slide 11
PC ALGORITHM
The PC algorithm found no links on the training data, as expected
Source: pca_pc_t2/outputs/tables/pc_variants_summary.csv, fig14_pc_sensitivity.csv; RESULTS.md section 3
11
Training data (planned)
0
0
Test data (final graph)
48
54
Flare rows only
51
55
Nonlinear test, 300 training rows
17
not run
With time lags (check only)
85
81
α = 0.05
α = 0.01
Number of links found
Training data gives 0 links because PCA makes the components uncorrelated there.
16 of 48
links in the final graph appear in at least 70% of 10 resamples
0.62
overlap between the graphs at α = 0.05 and α = 0.01
Notes: PCA makes its components uncorrelated on the data it was fitted to. So the PC algorithm sees no links there, which the plan predicted. We then ran four other versions. The one on test data became the final graph. Its links mostly reflect how far the test data has drifted from training, not cause and effect.

## Slide 12
LINKS BETWEEN UNITS
Most links connect NSU_NHT_CCR, ISOM and LOUP, but no root cause is found yet
Source: pca_pc_t2/outputs/tables/fig13_unit_level_graph.csv, root_cause_hypotheses.csv, pc_edges_stable.csv
12
ISOM
NSU_NHT_CCR
LOUP
PDA
PG
Top 8 links shown, line width = weight. No strong links for: SEU1, SEU2, SEU3, APS_NVPS_LEU, DAK, DIU, ISOM_3, ISOM_4.
Strongest links (weight from 0 to 1)
NSU_NHT_CCR → ISOM
0.93
ISOM → NSU_NHT_CCR
0.88
PDA → NSU_NHT_CCR
0.69
NSU_NHT_CCR → LOUP
0.61
LOUP → NSU_NHT_CCR
0.59
Root-cause trace for the alarm
At the alarm peak, component 24 rises most. It is led by PDA. No component points into it, so no root-cause unit can be named.
These links join components, not tags, and reflect drift as much as cause.
Notes: We turned the links between components into links between units, using how much each unit weighs in each component. The strongest links run between NSU_NHT_CCR, ISOM and LOUP, in both directions. The trace step found no upstream component for the alarm, so it names no root-cause unit.

## Slide 13
NEXT STEPS
We need three fixes before the next run, and two more after it
Source: pca_pc_t2/outputs/RESULTS.md (limitations and suggested next step)
13
1
Rebuild the flare labels
One event list per signal, checked against the operator log
2
Rebuild the normal baseline
Take months of non-flaring data that cover both operating states
3
Check tag 99PI3219
Find out if it is a sensor fault or a real change
4
Find the 42 missing tags
Confirm 418 against 376 with the data owner
5
Find links between tags
Use a method that handles time lags, such as PCMCI+, on flare windows
Needed before the next run
After that
Decision needed: approve fixes 1 to 3 so the next run gives results we can use.
Notes: Fixes 1 to 3 decide whether the next run can be read at all. Fix 4 is a short talk with the data owner. Fix 5 is the next step that RESULTS.md suggests, and it makes sense only after 1 to 3.