## Slide 1
Root cause detection for flaring
How two causal discovery methods work, and our first results on plant data
Progress review · 27 October 2026

## Slide 2: What this deck covers
Two separate parts. Part A explains methods on a toy example. Part B shows what we ran on plant data.
Root cause detection
PART A
Algorithm explainers
Studied on a toy example with a known answer. Not used on plant data yet.
PCMCI+, step by step
slide 5 – 15
VAR-LiNGAM, step by step
slide 16 – 24
The methods side by side
slide 25
PART B
Traditional PC on plant data
What we run today: PCA, then traditional PC, then T², on May 2025 data.
Our pipeline
slide 27
Data and PCA
slide 28 – 29
The causal graph
slide 30
Problems found
slide 31 – 33
Next steps
slide 34

## Slide 3: We want to find which process variables drive flaring
The plant records hundreds of tags every minute. We look for the ones that push the flare up.
Root cause detection
PLANT DATA
Hundreds of tags from 10 units, one reading per minute
CAUSAL DISCOVERY
Learn which variable affects which, as a graph
ROOT CAUSE
When a flare starts, find the variables that explain it
PART A · WHAT WE STUDIED
Two advanced methods, PCMCI+ and VAR-LiNGAM.
They handle time lags and same-minute effects.
Shown on a toy reactor with three sensors.
PART B · WHAT WE RAN
Traditional PC on one month of plant data.
PCA first, then PC, then T² to find the cause.
The pipeline runs, but the results need fixes.
NOTE Part B uses traditional PC. PCMCI+ and VAR-LiNGAM are not applied to plant data yet.

## Slide 4
PART A · ALGORITHM EXPLAINERS
How two advanced methods work
PCMCI+ and VAR-LiNGAM, on a toy reactor with three sensors. We made the data, so we know the true answer and can check every step.
These methods are studied only. We do not use them on plant data yet.

## Slide 5: The toy example: three reactor sensors
Three sensors on a reactor cooling loop, read once a minute for 300 minutes. We generated the data, so the true graph is known from the start.
THE THREE SENSORS
F
coolant flow
T
reactor temperature
P
vessel pressure
HOW THE DATA WAS MADE
F(t) = 0.60 F(t−1) + ε
T(t) = 0.65 T(t−1) + 0.50 F(t−1) + ε
P(t) = 0.80 T(t) + ε
ε is fresh noise, independent across sensors and across time.
THE TRUE GRAPH — FOUR LINKS, WHICH THE ALGORITHM MUST REDISCOVER
F
T
P
F
T
P
F
T
P
F → F and T → T one minute later, F → T one minute later, and T → P inside the same minute.
SETTINGS
τmax = 2
look back at most two minutes
N = 300
rows of data, 298 usable after cutting the lag
α = 0.01
a link is cut when the test cannot reject independence
partial correlation
the dependence measure used in every test
Part A · PCMCI+

## Slide 6: The pair we will follow: T and P
Every slide from here shows where this one pair stands. At the start the algorithm knows none of this.
WHAT THE ALGORITHM STARTS WITH
t−2
t−1
t
F
T
P
F
T
P
F
T
P
Every node at every past lag is a candidate cause of every present node. The three gold arrows are the ones that involve T and P.
WHAT THE ALGORITHM MUST WORK OUT ABOUT THIS PAIR
Cut T(t−1) → P(t)
Their plain correlation is 0.617, which looks like a strong lagged cause. It is not one.
Keep T(t) — P(t)
The only real link between the two sensors, and it acts inside a single minute.
Point it T(t) → P(t)
Surviving a test gives an edge, not an arrow. Direction comes last.
Part A · PCMCI+

## Slide 7: PCMCI+ in four pictures
Two estimation parts, then orientation. Each stage removes something from the picture before it.
EVERY CANDIDATE
t−2
t−1
t
F
T
P
F
T
P
F
T
P
Nothing has been ruled out. 21 possible links.
AFTER PART 1
F
T
P
F
T
P
F
T
P
A short lagged parent list per target. Same-instant links are untouched — part 1 never looks at them.
AFTER PART 2
F
T
P
F
T
P
F
T
P
Survivors of the MCI test. Adjacencies only, still no arrowheads.
AFTER ORIENTATION
F
T
P
F
T
P
F
T
P
Time orients the lagged links, one triple settles the last edge.
OUR PAIR gold marks T and P. The lagged arrow T(t−1) → P(t) survives part 1, dies in part 2, and the same-instant edge is the one that finally gets an arrowhead.
Part A · PCMCI+

## Slide 8: The basic test: partial correlation
Every removal in the whole algorithm is this picture. Only the contents of Z change.
WHAT THE TEST DOES
1
Pick a pair of columns, X and Y, and a set of other columns called Z.
2
From X, strip out everything the columns in Z can predict. Do the same to Y.
3
Correlate the two leftovers. That number is the partial correlation.
4
Near zero means Z explained the whole relationship, so the link is cut and this Z is kept as the pair’s separating set.
BEFORE
X
Y
shared
NOTHING LEFT → CUT
write Z down as the separating set
CUTTING AWAY Z
X
explained by Z
leftover
Y
explained by Z
leftover
The test looks only at the two leftovers.
SOMETHING LEFT → KEEP
the link survives into the next round
Part A · PCMCI+

## Slide 9: Part 1: build the parent list of P(t)
One target at a time. Only lagged nodes are candidates, so the same-instant node T(t) is not even in the running.
THE PROCEDURE
1
Correlate every candidate with the target, with nothing held fixed. Rank them, strongest first.
2
Take the strongest, T(t−1), and hold it fixed. Re-test every other candidate against the target.
3
Whatever collapses to near zero leaves the list for good. The rest stay.
4
Now hold pairs fixed, then triples, always strongest first, until no candidate has enough others left to pair with.
ROUND p = 0
t−2
t−1
t
F
T
P
F
T
P
F
T
P
Nothing held fixed. All six candidates survive — plain correlation cuts nothing.
ROUND p = 1
✕
✕
✕
F
T
P
F
T
P
F
T
P
T(t−1) held fixed. P(t−1), T(t−2) and P(t−2) collapse and leave.
ROUND p = 2
✕
F
T
P
F
T
P
F
T
P
T(t−1) and F(t−1) held fixed. F(t−2) collapses. Two candidates remain.
OUR PAIR T(t−1) was the strongest candidate, so it is the first thing put into Z — and it survives every round. Part 1 hands on B(P) = { F(t−1), T(t−1) }.
Part A · PCMCI+

## Slide 10: Why the Part 1 list is not final
Part 1 conditions on lagged nodes only, so it cannot block a path that passes through the present minute.
WHAT PART 1 KEPT FOR P(t)
t−2
t−1
t
F
T
P
F
T
P
F
T
P
Both arrows passed every lagged test, so both are on the list.
truth
WHAT IS ACTUALLY THERE
t−2
t−1
t
F
T
P
F
T
P
F
T
P
the mediator
Neither lagged node touches P directly. Both reach it through T(t), which sits at lag 0 — invisible to part 1.
OUR PAIR This is why T(t−1) → P(t) is still standing. To cut it, something has to put T(t) into Z. That is exactly what part 2 adds.
Part A · PCMCI+

## Slide 11: Part 2: build the test set Z for our link
Link under test: T(t−1) → P(t), in gold. Z is no longer a few candidates — it is assembled from three fixed sources.
F
T
P
F
T
P
F
T
P
t−2
t−1
t
parents of the TARGET
P(t) is the target, so B(P) goes in — minus the source itself. B(P) = {F(t−1), T(t−1)}, and T(t−1) is the link under test, so only F(t−1) is left.
parents of the SOURCE
T(t−1) is the source, so B(T) goes in as well, slid back to its own time slice.
S — same-instant neighbors
Nodes still adjacent to P at lag 0. S is empty in the first round and takes one more neighbor in each round after that.
OUR PAIR Once T(t) enters the gold box, our link can finally be cut.
Part A · PCMCI+

## Slide 12: A parent list moves back in time with its node
Part 1 reports every list as if its owner sat at time t. When that owner is the source of a lagged link, the list slides back with it.
AS PART 1 REPORTS IT
t−2
t−1
t
F
T
P
F
T
P
F
T
P
B(T) = { F(t−1), T(t−1) }, written for T sitting at time t.
slide back by τ = 1
AS PART 2 USES IT FOR OUR LINK
t−2
t−1
t
F
T
P
F
T
P
F
T
P
Here T is the source at t − 1, so the same list enters as { F(t−2), T(t−2) }.
OUR PAIR Stationarity is what makes the slide legal: one graph describes every minute, so a parent list can be moved along the time axis.
Part A · PCMCI+

## Slide 13: Part 2 rounds: where our link is removed
Grey ring = held fixed in Z for that round. Red dashes = cut in that round.
THE PROCEDURE
1
Start from the lagged links part 1 kept, plus every same-instant pair.
2
Round p: for each surviving link, build Z from both parent lists plus every S of size p drawn from the target’s same-instant neighbors.
3
A link dies at the first Z that zeroes its leftover. That Z is stored as the pair’s separating set.
4
Raise p and repeat until no target has enough neighbors left to fill S.
WHAT ENTERS
t−2
t−1
t
F
T
P
F
T
P
F
T
P
Six lagged links from part 1, plus the three same-instant pairs.
ROUND p = 0
✕
F
T
P
F
T
P
F
T
P
S is empty, but both parent lists are already in Z. The two false same-instant links collapse. Our link survives.
ROUND p = 1
✕
✕
F
T
P
F
T
P
F
T
P
S takes T(t). Both remaining arrows into P were only passing through it, so both are cut — ours included.
OUR PAIR T(t−1) → P(t) is gone, and the Z that killed it contained T(t). That note is written down — orientation is about to need it.
Part A · PCMCI+

## Slide 14: Orientation: give each link a direction
The skeleton has four edges and no arrowheads. Direction comes from the clock, then from one triple.
TIME SETTLES THREE
t−2
t−1
t
F
T
P
F
T
P
F
T
P
Anything crossing a time slice can only point forward. Three edges are directed without a single test.
THE TRIPLE
✕
F
T
P
F
T
P
F
T
P
T(t) ∈ the cutting set
T(t−1) → T(t) — P(t). The outer two are not adjacent, because we cut them in round 1, and T(t) was in the Z that cut them.
THE ONLY WAY LEFT
F
T
P
F
T
P
F
T
P
If the edge read P(t) → T(t), then T(t) would be a collider. A node inside the cutting set is never a collider, so the arrow points the other way.
OUR PAIR T(t) → P(t). The pair we picked at the start is finished, and the direction is the one the data was generated with.
Part A · PCMCI+

## Slide 15: The pair, from start to finish
Four moments in the life of one relationship — and the same four moments happened to every other link in parallel.
CANDIDATE
t−2
t−1
t
F
T
P
F
T
P
F
T
P
T(t−1) → P(t) and T(t) — P(t) both start as guesses, among 21.
SURVIVES PART 1
F
T
P
F
T
P
F
T
P
The lagged arrow is on B(P), because part 1 cannot see the mediator T(t).
CUT IN PART 2
✕
F
T
P
F
T
P
F
T
P
With T(t) in S, the lagged arrow drops to nothing and is cut. T(t) is recorded.
ORIENTED
F
T
P
F
T
P
F
T
P
That record makes the triple a non-collider, which forces T(t) → P(t).
RECOVERED GRAPH — the same four links as the equations on the setup slide, nothing extra, nothing missing
F
T
P
F
T
P
F
T
P
WHAT EACH PART BOUGHT
Part 1 a small, relevant Z for every later test
Part 2 a cut for every link that was only indirect
Orientation an arrowhead on what is left
Part A · PCMCI+

## Slide 16: Same reactor, one change: non-Gaussian noise
Three sensors on a reactor cooling loop, read once a minute for 300 minutes. Only the noise distribution has changed.
THE THREE SENSORS
F
coolant flow
l/min
T
reactor temperature
°C
P
vessel pressure
bar
HOW THE DATA WAS MADE
F(t) = 0.60 F(t−1) + ε
T(t) = 0.65 T(t−1) + 0.50 F(t−1) + ε
P(t) = 0.80 T(t) + ε
same minute
ε is uniform noise, independent across sensors and across time — not Gaussian. That one change is what VAR-LiNGAM feeds on.
THE FIRST SIX MINUTES OF THE RECORDING
minute
F l/min
T °C
P bar
1
40.69
309.52
11.83
2
39.88
308.72
10.89
3
38.37
308.85
11.91
4
40.17
309.60
11.69
5
39.67
308.63
11.11
6
39.19
308.00
9.03
300 rows in total · 299 usable once one lag is cut off the front
SETTINGS
τmax = 1
one minute of memory covers the true delays
N = 300
rows, estimated by ordinary least squares
excess kurtosis −1.14, −1.09, −0.60
the residuals are flat-topped, far from Gaussian
prune at |b| < 0.05
anything smaller is read as estimation noise
Part A · VAR-LiNGAM
Notes: Same three sensors and the same generating equations as the PCMCI+ half. The only difference is that the shocks are uniform, not Gaussian.

## Slide 17: Two kinds of link need different tools
A lagged link is ordered by the clock. A same-minute link is not, so the algorithm has to read the shape of the noise instead.
LAGGED — THE CLOCK DECIDES
t − 1
F
T
P
t
F
T
P
A cause in an earlier minute cannot be the effect of a later one. Nothing has to be tested — the direction is given.
SAME MINUTE — THE CLOCK IS SILENT
T
P
T
P
corr( nT , nP ) = 0.771
One number, two stories. A correlation is symmetric, so least squares alone can never choose between these two arrows.
THE NEW INGREDIENT
one shock
two shocks added together
Adding independent shocks pulls the shape toward a bell. So the direction whose leftover stays un-bell-like, and independent of its predictor, is the one that un-mixed the data.
OUR PAIR
We follow T and P again — the same pair the PCMCI+ half followed, settled here by a completely different argument.
Part A · VAR-LiNGAM
Notes: Motivation slide. The whole algorithm exists because lag-0 links carry no time ordering.

## Slide 18: The model in two forms
Two ways to write the same process. A VAR fits the second one, and the algorithm is the trip back to the first.
WHAT THE PROCESS ACTUALLY OBEYS — STRUCTURAL FORM
x(t) = B₀ x(t) + Στ Bτ x(t−τ) + e(t)
B₀ same-minute weights
Bτ lagged weights
e(t) independent, non-Gaussian shocks
WHAT A VAR CAN FIT — REDUCED FORM
x(t) = Στ Mτ x(t−τ) + n(t)
No term on the right is dated t, so this is pure prediction from the past. Everything that happens inside the minute is pushed into the residual n(t).
THE BRIDGE
e(t)
( I − B₀ )⁻¹
n(t)
the VAR residual is a mixture of the true shocks
Mτ = ( I − B₀ )⁻¹ Bτ
Bτ = ( I − B₀ ) Mτ
WHAT MUST BE TRUE
B₀ is acyclic — the same-minute links admit an ordering
the shocks are mutually independent — no hidden common cause
the shocks are non-Gaussian — otherwise the lag-0 order is unidentifiable
the process is stationary over the window
the lag order τmax is large enough to hold the real delays
Part A · VAR-LiNGAM
Notes: The identity B_tau = (I - B0) M_tau is the whole reason the algorithm works. Everything else is estimation.

## Slide 19: VAR-LiNGAM in four pictures
Fit the past, read the leftovers, order the minute, then undo the mixing. Each stage adds something the one before it could not see.
1 · VAR FIT
t − 1
F
T
P
t
F
T
P
Everything the past can explain, with no same-minute term allowed. P picks up two lagged links it does not really have.
2 · THE RESIDUALS
t − 1
F
T
P
t
F
T
P
nF
nT
nP
What is left is a mixture of the true shocks. The T and P residuals still move together.
3 · LiNGAM ON n(t)
t − 1
F
T
P
t
F
T
P
order F → T → P
Independence picks the same-minute order, and B₀ becomes triangular in it.
4 · CONVERT AND PRUNE
t − 1
F
T
P
t
F
T
P
( I − B₀ ) Mτ removes the contamination, and small weights are dropped.
OUR PAIR
T(t−1) → P(t) appears in picture 1 and is gone by picture 4 — not cut by a test, but cancelled by an identity.
Part A · VAR-LiNGAM
Notes: Overview slide. Panels 1 and 4 are the before and after of the same graph.

## Slide 20: Step 1: fit the VAR and keep the residuals
Ordinary least squares, one equation per sensor. The output is a prediction matrix and a residual column for each sensor.
THE PROCEDURE
1
Center every column, then regress x(t) on x(t−1) by ordinary least squares.
2
Collect the coefficients into M₁. This is prediction, not yet structure.
3
Keep the residuals n(t) = x(t) − M₁ x(t−1), one column per sensor.
4
Check that the residuals are non-Gaussian. If they are not, stop — the next step cannot work.
M₁ — WHAT THE PAST PREDICTS
F
T
P
F
T
P
0.572
-0.018
0.001
0.513
0.646
-0.037
0.436
0.553
-0.062
rows = target at t · columns = source at t − 1
Row P says that both F(t−1) and T(t−1) predict pressure. Neither link exists in the equations that made the data. They are the same-minute arrow T(t) → P(t), seen through one lag.
CORRELATION OF THE RESIDUALS
F
T
P
F
T
P
1.000
0.003
0.015
0.003
1.000
0.771
0.015
0.771
1.000
excess kurtosis −1.14 −1.09 −0.60
If the VAR were the whole story these columns would be independent. F is clean, but T and P share 0.771. That leftover dependence is the same-minute link, and it is what step 2 works on.
OUR PAIR
The VAR scores T(t−1) → P(t) at 0.553 and cannot tell that the number is borrowed.
Part A · VAR-LiNGAM
Notes: M1 is a prediction object. Row P carries contamination from the instantaneous link.

## Slide 21: Step 2a: how one direction is decided
This one test is the whole of LiNGAM. Regress one residual on another, then ask whether the leftover is independent of what you regressed on.
THE TEST
1
Take the two residual columns and assume a direction, say T causes P.
2
Regress the second residual on the first by least squares and keep the leftover.
3
Measure the dependence between the leftover and the predictor. Zero means independent.
4
Do the same the other way. The direction with the smaller dependence is the cause.
DIRECTION A — T(t) → P(t)
slope = 0.831
leftover (vertical) against predictor (horizontal)
dependence
0.0051
leftover kurtosis
-1.20
An even band. The spread does not change across the plot, and the leftover is still as flat-topped as the original shock.
KEEP
DIRECTION B — P(t) → T(t)
slope = 0.715
leftover (vertical) against predictor (horizontal)
dependence
0.0464
leftover kurtosis
-0.71
Pinched at both ends. The spread depends on the predictor, and the leftover has drifted toward a bell.
REJECT
OUR PAIR
Nine times more dependence the wrong way round. T(t) → P(t) — the same arrow the PCMCI+ half reached through a collider rule.
Part A · VAR-LiNGAM
Notes: Dependence is a normalised HSIC. Zero means independent.

## Slide 22: Step 2b: find the order, one sensor at a time
A sensor with no same-minute parent leaves no trace in anything it explains. Find it, remove it, repeat.
THE PROCEDURE
1
For each remaining sensor, regress every other one on it and score the worst dependence left behind.
2
The lowest score has no same-minute parent. It goes next in the order.
3
Replace every other column by its leftover after removing that sensor.
4
Repeat on what remains. Then regress each sensor on its predecessors to fill B₀.
ROUND 1
worst dependence as root
F
chosen
0.0030
T
not yet
0.0051
P
not yet
0.0464
P leaves 0.0464 behind in T, so it cannot be first. F and T both sit near zero because no same-minute link joins them, so either may go first.
ROUND 2
worst dependence as root
T
chosen
0.0050
P
not yet
0.0457
After F is removed, P still leaves 0.0457 in T. T is next.
ROUND 3
worst dependence as root
P
chosen
—
Only P is left, so it takes the last place. Order: F → T → P.
OUR PAIR
Regressing on predecessors gives B₀ = 0.831 for T(t) → P(t), with 0.003 and 0.016 everywhere else below the diagonal.
Part A · VAR-LiNGAM
Notes: F and T tie because there is no lag-0 edge between them. Any order with P last yields the same B0.

## Slide 23: Steps 3 and 4: correct the lagged weights, then prune
B₀ is known, so the contaminated lagged weights can be corrected in one multiplication.
THE IDENTITY, APPLIED
B₁ = ( I − B₀ ) M₁
1
0
0
−0.003
1
0
−0.016
−0.831
1
·
0.572
-0.018
0.001
0.513
0.646
-0.037
0.436
0.553
-0.062
=
THE ROW THAT MATTERS — PRESSURE
−0.016 × 0.572 − 0.831 × 0.513 + 0.436 = 0.001
−0.016 × −0.018 − 0.831 × 0.646 + 0.553 = 0.016
Both lagged links into pressure collapse to nothing. They were never separate effects — they were T(t) → P(t) counted twice.
AFTER PRUNING AT |b| < 0.05
B₀ same minute
F
T
P
F
T
P
0.000
0.000
0.000
0.003
0.000
0.000
0.016
0.831
0.000
one survivor
0.831
B₁ one minute back
F
T
P
F
T
P
0.572
-0.018
0.001
0.511
0.646
-0.037
0.001
0.016
-0.031
three survivors
0.572 0.511 0.646
green kept · red dropped as estimation noise
OUR PAIR
T(t−1) → P(t) falls from 0.553 to 0.016 and is pruned. PCMCI+ cut it with a conditioning set. Here an identity does it.
Part A · VAR-LiNGAM
Notes: Adaptive lasso or bootstrap thresholds replace the fixed cut-off in production use.

## Slide 24: The recovered graph matches the true graph
Four weighted links, the same four the equations on the setup slide put in, with the numbers attached.
RECOVERED GRAPH — WEIGHTS ESTIMATED, TRUTH IN BRACKETS
minute t − 1
F
T
P
minute t
F
T
P
0.831
estimated (true)
F(t−1) → F(t)
0.572
(0.60)
F(t−1) → T(t)
0.511
(0.50)
T(t−1) → T(t)
0.646
(0.65)
T(t) → P(t)
0.831
(0.80)
Nothing extra, nothing missing. The same four links the PCMCI+ half recovered, now carrying effect sizes.
HOW TO READ A WEIGHT
A one-unit change in the parent moves the child by b units, with every other parent held fixed. These are structural coefficients, not correlations.
T(t) → P(t) b = 0.831
One degree hotter raises pressure by 0.83 bar inside the same minute. A lag-0 arrow is relative to the sampling interval — read at one second instead, this link would move to lag 1.
WHAT EACH STEP BOUGHT
VAR
everything the past can explain, and clean residuals
LiNGAM
the order inside the minute, and B₀
Convert
lagged weights with the same-minute leak removed
Prune
a graph instead of a dense matrix
WHEN IT BREAKS
residuals close to Gaussian — the lag-0 order stops being identifiable
a hidden common cause — the shocks are no longer independent
τmax too small, or sampling slower than the true delay
Part A · VAR-LiNGAM
Notes: The first failure mode is the live one on the Tennessee Eastman data, where VAR residuals are close to Gaussian.

## Slide 25: PCMCI+ and VAR-LiNGAM side by side
Both recover the four true links of the toy reactor. Traditional PC, used in Part B, has neither of their extras.
Part A · Comparison
Traditional PC
USED IN PART B
No. Each row is treated as independent.
Conditional independence tests
Collider rules. Some edges can stay undirected.
A graph, no weights
Enough data per test, no hidden common cause
PCMCI+
PART A
Yes, up to τmax (2 in the toy).
Conditional independence tests, in two parts
Time order, then collider rules
A graph, no weights
Same graph every minute (stationary)
VAR-LiNGAM
PART A
Yes, through the VAR (τmax 1 in the toy).
Regression, then an independence check on residuals
Time order, then the shape of the noise
A graph with link weights
Non-Gaussian noise, no hidden common cause
TIME LAGS
MAIN TOOL
SAME-MINUTE DIRECTION
OUTPUT
NEEDS

## Slide 26
PART B · RUNNING THE ALGORITHM ON PLANT DATA
Traditional PC on plant data
One month of plant data: May 2025, one reading per minute. PCA reduces the tags, traditional PC builds the graph, and T² looks for the cause of alarms.
We use traditional PC here, not PCMCI+ or VAR-LiNGAM.

## Slide 27: Our pipeline: PCA, then PC, then T²
Five stages. All seven scripts passed their checks, and the full run took under 30 seconds.
1
Load and clean
298 tags in, 273 kept
1-minute grid, 44,640 rows
2
PCA
270 process tags
→ 26 components (PCs)
3
Traditional PC
26 PCs + 3 flare tags
Rule: a flare tag causes nothing
4
Make a DAG
Pick one direction
for every edge
5
T² decomposition
Alarm when T² is high
then ask which node is to blame
HOW WE RUN TRADITIONAL PC
causal-learn PC, Fisher-Z test, alpha 0.01
Depth up to 3, every 10th row (4,464 rows)
36,308 tests, 2 seconds
No time lags: each minute is treated as independent
T² DECOMPOSITION
Method from Li, Jin and Shi (2008)
Alarm when T² > 42.6
A node is to blame when its term > 3.13
Normal behaviour is learned from a reference period
Part B · Plant data
Source: pca_pc_t2/outputs/SUMMARY.md, logs/

## Slide 28: From 298 tags to 29 model inputs
Cleaning removed 25 tags. PCA then squeezed 270 process tags into 26 components.
298
tags loaded · 294 process + 4 flare, from 10 units
273
tags after cleaning · 25 dropped (see right)
270 + 3
into the model · 270 process tags go to PCA, 3 flare tags go straight to PC
29
graph nodes · 26 PCs + 3 flare tags
WHY 25 TAGS WERE DROPPED
Constant
10
Too much missing data
8
Almost constant
6
Constant in the reference
1
WHAT THE DATA LOOKS LIKE
1 to 31 May 2025, one row per minute: 44,640 rows
Only 2 short gaps were filled; nothing else imputed
1 of 4 flare tags dropped: 44FT2505 is 64.5% missing
Part B · Plant data
Source: pca_pc_t2/outputs/data/s1_summary.json, logs/s1_load_clean.log

## Slide 29: 26 PCs keep 80% of the variance
The variance is spread thin: PC1 holds only 19.6%. The LOUP unit leads most of the first PCs.
CUMULATIVE VARIANCE KEPT, %
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
Cumulative | 19.6 | 32 | 41.1 | 47.1 | 51.9 | 55.2 | 58.5 | 60.7 | 62.9 | 64.8 | 66.6 | 68 | 69.4 | 70.6 | 71.8 | 72.8 | 73.8 | 74.6 | 75.5 | 76.3 | 77 | 77.7 | 78.3 | 78.9 | 79.5 | 80.1
19.6%
PC1 alone
64.8%
first 10 PCs
80.1%
all 26 PCs
component number
SHARE OF EACH PC'S LOADINGS BY UNIT, %
LOUP
ISOM
PG
DIU
PDA
SEU1
SEU2
SEU3
ISOM3
DAK
PC1
27
12
12
13
9
10
6
3
3
5
PC2
29
11
19
6
5
18
4
1
5
1
PC3
18
24
33
2
11
3
1
2
2
5
PC4
14
5
17
22
12
8
16
3
1
1
PC5
29
8
7
6
7
16
5
4
18
0
PC6
18
22
12
4
15
8
6
9
4
2
PC7
57
14
6
2
4
8
3
4
1
0
PC8
12
12
7
3
10
5
4
10
37
1
PC9
24
42
4
4
6
5
6
6
3
0
PC10
12
36
7
3
10
6
8
8
8
0
Darker = larger share. Bold = the leading unit of that PC.
Part B · Plant data
Source: pca_pc_t2/outputs/data/pca_variance.csv, tables/pca_unit_share.csv

## Slide 30: All 50 graph edges go from a PC to a flare tag
There is no edge between two PCs. So the graph is really three regressions, one per flare tag.
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
26 PCs (all are roots: nothing points into them)
LR flare sum 16 parents
509FI5201 15 parents
509MW5101 19 parents
Line width = size of the effect. Strongest edge, in gold: PC2 → LR flare sum (weight -0.62).
WHY NO PC-PC EDGES
PCA makes components uncorrelated by design. So the PC test finds no link between them. This is expected, not a bug.
WHAT THIS MEANS
The graph cannot show a chain like A → B → flare. It only says which PCs move with each flare tag.
STABLE WITH ALPHA
With alpha 0.05 we get 55 edges, again all PC → flare. No flare tag points to anything.
Part B · Plant data
Source: pca_pc_t2/outputs/graph/dag_edges.csv, t2/coefficients.csv, tables/pc_alpha_sweep.csv

## Slide 31: The flare rule turns the whole month into one event
A minute is flagged when a flare tag is above median + 3 × MAD. Flags less than 5 minutes apart are joined.
MAY 2025, ONE BAR PER STEP
1 May
8 May
15 May
22 May
29 May
Flagged minutes
before joining
15.9% of all minutes (total length, not their real positions)
Flare events
after joining
1 event: 1 May 01:29 to 31 May 20:30 · 99.3% of all rows
Only about 298 minutes in the whole month count as 'no flare'.
SHARE OF MINUTES ABOVE THE THRESHOLD
44FT2505 (dropped later)
0.52%
LR flare sum
7.32%
509FI5201
8.67%
509MW5101
0.07%
WHY THIS MATTERS
There is no flare-free period to learn normal behaviour from.
So the reference became the first 60% of May (to 19 May 14:23), with flares inside it.
Part B · Plant data
Source: pca_pc_t2/outputs/data/flare_events.csv, tables/flare_thresholds.csv, data/deviations.json

## Slide 32: The T² alarms do not behave as expected
Alarms are far too common in the reference period, and the decomposition does not add up when it matters.
SHARE OF ROWS WITH A T² ALARM, %
13.0%
Reference rows
46.4%
All rows
46.1%
Flare rows
98.7%
No-flare rows (~298)
Dashed line: reference rows should alarm about 5% of the time. No-flare rows alarm more than flare rows.
DOES THE DECOMPOSITION ADD UP?
The node terms should sum to the total T². We measure the gap (0 = perfect).
0.13
median gap,
reference rows
0.92
median gap,
alarm rows
THE NORMAL-PERIOD TERMS ARE NOT NORMAL
0.61% of reference values pass the limit; 0.17% expected
Flare tags have very heavy tails (excess kurtosis 50 and 15)
Likely cause: the reference period has flares in it (not yet checked)
Part B · Plant data
Source: pca_pc_t2/outputs/data/s5_summary.json, tables/reference_check.csv

## Slide 33: What the T² points to, and why we cannot trust it yet
We count how often each node is to blame during a T² alarm. These are leads, not answers.
NODE IS TO BLAME, % OF ALARM ROWS
PC1 (LOUP)
16.9%
LR flare sum (flare)
13.4%
509MW5101 (flare)
10.6%
509FI5201 (flare)
9.0%
PC14 (SEU3)
7.1%
PC12 (PDA)
5.5%
PC9 (ISOM)
2.9%
PC8 (ISOM_3)
2.9%
■ PC (main unit) ■ flare tag
PC7 FIRES IN NORMAL TIMES TOO
PC7 is to blame in 4.7% of reference rows, but only 2.2% of alarm rows. It is noise, not a flare signal.
THE 'FIRST ALARM' IS THE FIRST MINUTE
The single event's first alarm is at 1 May 00:00, the start of the data. So PC13 and PC7, flagged there, do not mark a flare start.
ONE LEAD WORTH CHECKING
PC14 loads on SEU3 pressure tags 42PC4215 and 42PC4501 (0.31 each). PC1 is spread over many units (about 0.11 per tag), so it names no single tag.
Part B · Plant data
Source: pca_pc_t2/outputs/tables/root_cause_nodes.csv, tables/root_cause_by_event.csv

## Slide 34: Next steps: fix the data setup, then rerun
The pipeline works. The inputs to it need fixing before the root causes can be read.
pca_pc_t2 · PCA + traditional PC + T²
1
Fix the flare rule so that flares become separate events
2
Find a flare-free reference period to learn normal behaviour
3
Check the unit folder names in .env (3 units were not found)
4
Rerun. Check: reference alarms near 5%, decomposition gap small
5
Then read the root causes, starting with PC14 and the SEU3 tags
causal_t2 · traditional PC on all 267 tags
1
The PC stage crashed: an IndexError after 827 s, then a segfault
2
It has about 13 million tests even at depth 1
3
Run the three checks in command.md: traceback, one-thread run, versions
4
Pick the fix from the result: threading, memory, or library version
Part B · Plant data
Source: pca_pc_t2/outputs/SUMMARY.md, causal_t2/outputs/LOG.md, command.md